# Connecting Intercom to the SONY CCU-TX50

## Overview

The CCU-TX50 supports 2 wire (RTS or ClearCom) and 4 wire interfaces.

The type of interface is set with switches on the AU-300 Board and by connecting to the appropriate pins

on the 25 pin female D sub connector on the rear panel. Two channels of intercom can be accommodated,

one called Engineering, the other Production.

## Common Information

### Pinouts / Connectors

Intercom / Tally / PGM connector pinout:

| Pin | Signal | Pin | Signal |
| --- | --- | --- | --- |
| 1 | Engineering (R, X, OUT) | 14 | Production (R, X, OUT) |
| 2 | Engineering (R, Y, OUT) | 15 | Production (R, Y, OUT) |
| 3 | Engineering GND | 16 | Production GND |
| 4 | Engineering (T, X, IN) | 17 | Production (T, X, IN) |
| 5 | Engineering (T, Y, IN) | 18 | Production (T, Y, IN) |
| 6 | PGM (X) IN | 19 | No connection |
| 7 | PGM (Y) IN | 20 | No connection |
| 8 | PGM (G) IN | 21 | No connection |
| 9 | Ground | 22 | AUX 4 |
| 10 | AUX 3 | 23 | AUX 5 |
| 11 | R Tally (X) IN | 24 | G Tally (X) IN |
| 12 | R Tally (Y) IN | 25 | G Tally (Y) IN |
| 13 | Ground |  |  |

The mating connector is shown here (25 pin Male as seen from soldering side):

### Switch Locations

## RTS Connections

Connect to pins 1 and 3 to use the Engineering channel, pins 14 and 16 to use the Production channel.

Set S204 and S205 on the AU-300 Board to “RTS”.

## ClearCom Connections

Connect to pins 1 and 3 to use the Engineering channel, pins 14 and 16 to use the Production channel.

Set S204 and S205 on the AU-300 Board to “CC” (DOWN).

## 4 wire Connections

Connect the receive side to pins 1 and 2 for Engineering, 14 and 15 for Production.

Connect the transmit side to pins 4 and 5 for Engineering, 17 and 18 for Production.

Set S206 and S207 on the AU-300 Board to “4W” (UP).